## Slide 1: Harsh Environment Sensor Board (Part II)
Joseph Portera, Jordan Anger, Jasper Everitt, Anthony Sedore

## Slide 2: Introduction
The Harsh Environment Sensor Board is a hardware and software solution aimed at monitoring and reporting telemetry data from various sensors to remote operators. This PCB is meant to be small and efficient for clients who need to monitor systems in harsh environmental conditions. It reports its data through cellular networks to users.

## Slide 3: Requirements
Product must be able to operate between -30° and 150° degrees Fahrenheit -Use temperature resistant electronics and encase in an enclosure
Product must read environmental data with sensors -Sensors will be connected to the PCB and controlled with microcontroller
Product shall transmit data over cellular transmission -Cellular transmission module will be connected to the PCB and controlled with microcontroller
Product will operate through an 18650 Li-ion battery -Implement 18650 hardware and battery management system
Product shall communicate with external sensors -Separate connection to the PCB will connect with external sensors
Product shall have battery charging capabilities -Battery recharging circuit integrated onto PCB with Voltage Regulator
Product must read board temperature -Sensor integrated onto PCB that can read current temperature

## Slide 4: System Diagram
ESP-32
Lithium Battery Interface
18650
5V Bus
USB-C
Serial DATA
Converter
24VDC Input
Analog Signal Input
Temp 1
5VDC Input
3.3v Regulator
RST_CMD
CFG_CMD
Networking CCA (4G LTE)
SLP_CMD
BOOT_CMD
3.3V
3.3v
5v
5v
5v
4.1v
5v
status
High/Low
High/Low
High/Low
High/Low
Compressed Data
Ser Data
Analog Volts
Analog Volts
Ser Data
3.3v
Ser Data

## Slide 5: System Diagram

## Slide 6: Technical Trades
Power Source Selection:
  Trade: Choosing between a rechargeable 18650 battery versus a non-rechargeable but higher capacity alternative
  Rationale: The rechargeable battery was selected for its balance between power capacity and sustainability, allowing for long-term use without the need for frequent replacements in remote locations
Communication Protocols:
  Trade: Implementing a 4G LTE module as opposed to a lower power but shorter range communication option like LoRa
  Rationale: 4G LTE was chosen for its widespread availability and reliability in data transmission, ensuring remote monitoring capabilities without significant geographical limitations
Enclosure Material:
  Trade: Selection of enclosure material considering factors such as thermal resistance, weight, and durability
  Rationale: The chosen material provides an optimal balance between thermal insulation, structural integrity, and weight, making it suitable for various harsh environments
Temperature Range Adaptability:
  Trade: Designing for the extreme temperature range with trade-offs between component cost and operating range
  Rationale: The chosen components offer the best compromise between the ability to withstand extreme temperatures and cost-effectiveness

## Slide 7: SWaP and Performance
Size
  PCB Size - 2.3” x 3.6”
  Enclosure – 7.87" x 4.72" x 2.95"
Weight
  Two 18650 Cells: 45g * 2 = 90g
  Weight of 4-Layer PCB & Components = 73 g
  Waterproof ABS Plastic Enclosure = 43 g
  Total Weight = 206 g (0.45 pounds)
Power Requirements
  Capacity of 14 Wh for one 18650 Cell = 14 Wh * 2 = 28 Wh
  ESP32 Microcontroller sleep energy consumption of 0.8mA, 240mA transmitting WiFi
  Estimated Power Consumption of 1w, Battery Lifespan of ~1 Days
    Transmission Time of 60 seconds per hour
Performance
  One Day on battery power with full capabilities, or could be extended to 2 days in a low power state.

## Slide 8: Testing and Integration

## Slide 9: Risks
Component and PCB prototype delivery not arriving on time
Finalize bill of materials and components so orders can be placed sooner
Component Shortages
Choose parts with lots of stock
Order parts early
Identify Alternatives
Assembly of prototype
Make sure to use functional pick and place machines
Failure of cellular data transmission
Incorporate interface onto PCB to directly obtain data if cellular transmission fails
Sensor Interface Accommodations
PCB will be designed to fit standard sensor interface designed by Software Logistics
PCB doesn’t work as intended
Conduct extensive analysis of systems and plan to have extra time for additional PCBs
Verification for correct use of different components using data sheets

## Slide 10: Risk Analysis
Most Critical Risks
  Failure of initial PCB’s
  Failure of cellular communication
  Integrating all systems of the PCB together

## Slide 11: Risk Mitigation
Most Critical Risks
  Failure of initial PCB’s
  Failure of cellular communication
  Integrating all systems of the PCB together
Mitigation Plans
  Build small prototypes to test on first. Order multiple PCBs. Order PCB’s ahead of schedule.
  Test communication system before implementing onto PCB
  Perform checks on PCB design and simulate to evaluate all systems are integrated.

## Slide 12: Project Schedule

## Slide 13: Bill Of Materials

## Slide 14: Action Register